## Slide 1
UCIe™
(Universal Chiplet Interconnect Express™)
Building an open ecosystem of chiplets
for on-package innovations
Presented by
UCIe Promoters

## Slide 2
Moore Predicted
“Day of Reckoning”
  “It may prove to be more economical to build large systems out of smaller functions, which are separately packaged and interconnected.”*
  - Gordon E. Moore
*“Cramming more components onto integrated circuits,” Electronics, Volume 38, Number 8, April 19, 1965
2

## Slide 3
Enables construction of SoCs that exceed maximum reticle size
  Package becomes new System-on-a-Chip (SoC) with same dies (Scale Up)
Reduces time-to-solution (e.g., enables die reuse)
Lowers portfolio cost (product & project)
  Enables optimal process technologies
  Smaller (better yield)
  Reduces IP porting costs
  Lowers product SKU cost
Enables a customizable, standard-based product for specific use cases (bespoke solutions)
Scales innovation (manufacturing and process locked IPs)
Align Industry around an open platform to enable chiplet based solutions
OPEN CHIPLET: PLATFORM ON A PACKAGE
High-Speed Standardized
Chip-to-Chip Interface (UCIe)
Customer IP &
Customized Chiplets
Sea of Cores
(heterogeneous)
Advanced 2D/2.5D/3D Packaging
Heterogeneous Integration Fueled by an Open Chiplet Ecosystem
(Mix-and-match chiplets from different process nodes / fabs / companies / assembly)
3
Motivation
20X I/O Performance at 1/20th Power vs off-package SerDes at Launch
Gap more prominent with better on-package technologies in future
Memory

## Slide 4
UCIe - Architected and specified from the ground-up to deliver the best KPIs while meeting wide adoption criteria
Key Performance Indicators
  Bandwidth density (linear & area)
    Data Rate & Bump Pitch
  Energy Efficiency (pJ/b)
    Scalable energy consumption
    Low idle power (entry/exit time)
  Latency (end-to-end: Tx+Rx)
  Channel Reach
    Technology, frequency, & BER
  Reliability & Availability
  Cost
    Standard vs advanced packaging
Key Metrics and Adoption Criteria
Factors Affecting Wide Adoption
  Interoperability
    Full-stack, plug-and-play with existing s/w is+
    Different usages/segments
    Technology
      Across process nodes & packaging options
      Power delivery & cooling
      Repair strategy (failure/yield improvement)
      Debug – controllability & observability
    Broad industry support / Open ecosystem
      Learnings from other standards efforts
4

## Slide 5
(Different flavors of packaging options supported to build an open ecosystem)
Jumpstarting UCIe
Intel donates initial specification
PROTOCOL LAYER
DIE-TO-DIE ADAPTER
PHYSICAL LAYER
LINK TRAINING
LANE REPAIR (when applicable)
LANE REVERSAL (when applicable)
SCRAMBLING/DE-SCRAMBLING (opt-in)
SIDEBAND TRAINING & TRANSFERS
ANALOG FRONT END
CLOCK FORWARD
ARB/MUX (when applicable)
CRC/RETRY (when applicable)
LINK STATE MANAGEMENT
PARAMETER NEGOTIATION
FIT AWARE / D2D INTERFACE (FDI)
RAW D2D INTERFACE (RDI)
STANDARD SPECIFICATIONS
Physical Layers
Initial D2D I/O
Protocols
CXL™/PCIe®
Form Factors
Management
Focus of UCIe 1.0 Specification
  Physical Layer: Die-to-Die I/O with industry-leading KPIs
  Protocol: CXL™/PCIe® for near term volume attach
    SoC construction issues are addressed since CXL/PCIe is a board-to-board interface
    CXL/PCIe addresses common use cases
      I/O attach with PCIe/CXL.io
      Memory use cases: CXL.mem
      Accelerator use cases: CXL.cache
  Well defined specification: ensure interoperability and future evolution
Future: the chiplet journey is just starting!!
  Other protocols
  Advanced Chiplet form-factors (e.g., 3D)
  Chiplet management
  More to come ….
Die
-
2
Package Substrate
Die
-
0
Die
-
1
Silicon Bridge
(e.g. EMIB)
Silicon Bridge
(e.g. EMIB)
Die
-
2
Die
-
0
Package Substrate
Interposer (e.g. CoWoS)
Die
-
1
Die
-
2
Package Substrate
Die
-
0
Die
-
1
5
(Standard Package)
(Multiple Advanced Package Choices)

## Slide 6
SoC Package level construction for wide range of usages from Hand-held to high-end servers
Mix and match dies from multiple sources with different packaging options
CXL Pooled Memory/
Storage
Compute
Compute
Compute
X
HDD
  
HDD
X
SSD
  
SSD
X
CPU
  
CPU
X
TORS
(Compute Drawer)
(w/ UCIe-based SoCs)
(Memory/ Storage Drawer)
(w/ UCIe-based SoCs)
Provision to extend off-package with UCIe Retimers connecting to other media (e.g., optics, electrical cable, mmWave)
UCIe / CXL through UCIe Retimer
Usage Models Supported by UCIe

## Slide 7
Characteristics / KPIs
Data / Outcome
Standard Package
Your Key Performance Indicator goes here
Add a few details describing the related activities
  What results did you obtain from your project?
  Write them here.
  What results did you obtain from your project?
  Write them here.
  What results did you obtain from your project?
  Write them here.
Your Key Performance Indicator goes here
Your Key Performance Indicator goes here
Add a few details describing the related activities
Add a few details describing the related activities
UCIe 1.0: Characteristics and Key Metrics
Data / Outcome
CHARACTERISTICS | STANDARD PACKAGE | ADVANCED PACKAGE | COMMENTS
Data Rate (GT/s) | 4, 8, 12, 16, 24, 32 |  | Lower speeds must be supported -interop (e.g., 4, 8, 12 for 12G device)
Width (each cluster) | 16 | 64 | Width degradation in Standard, spare lanes in Advanced
Bump Pitch (um) | 100 – 130 | 25 - 55 | Interoperate across bump pitches in each package type across nodes
Channel Reach (mm) | <= 25 | <=2 | 
KPIs / TARGET FOR KEY METRICS | STANDARD PACKAGE | ADVANCED PACKAGE | COMMENTS
B/W Shoreline (GB/s/mm) | 28 – 224 | 165 – 1317 | Conservatively estimated: AP: 45u; Standard: 110u; Proportionate to data rate (4G – 32G)
B/W Density (GB/s/mm2) | 22-125 | 188-1350 | 
Power Efficiency target (pJ/b) | 0.5 | 0.25 | 
Low-power entry/exit latency | 0.5ns <=16G, 0.5-1ns >=24G |  | Power savings estimated at >= 85%
Latency (Tx + Rx) | < 2ns |  | Includes D2D Adapter and PHY (FDI to bump and back)
Reliability (FIT) | 0 < FIT (Failure In Time) << 1 |  | FIT: #failures in a billion hours (expecting ~1E-10) w/ UCIe Flit Mode
UCIe 1.0 delivers the best KPIs while meeting the projected needs for the next 5-6 years.
Wide industry leader adoption spanning semiconductor, manufacturing, assembly, & cloud segments.
7

## Slide 8
Board Members
Leaders in semiconductors, packaging, IP suppliers, foundries, and cloud service providers are joining together to drive
The open chiplet ecosystem.
JOIN US!
8

## Slide 9
Leaders in semiconductors, packaging, IP suppliers, foundries, cloud service providers join forces to launch Universal Chiplet Interconnect Express (UCIe) technology to standardize the chiplet ecosystem today and future generations of chiplet technology.
New open standard establishes an open chiplet ecosystem and ubiquitous interconnect at the package level.
  UCIe 1.0 Specification ratified to provide a complete standardized die-to-die interconnect with physical layer, protocol stack, software model, and compliance testing that will enable end users to easily mix and match chiplet components from a multi-vendor ecosystem for System-on-Chip (SoC) construction, including customized SoC.
  The specification is available to the public https://www.uciexpress.org/specification
UCIe Consortium is officially incorporated and welcomes interested companies and institutions to join the organization at the Contributor and Adopter level.
Established 5 Technical Working Groups (Electrical, Protocol, Form Factor/Compliance, Manageability / Security, Systems and Software) and Marketing Working Group
Learn more by visiting www.UCIexpress.org
Summary
9

## Slide 10
Thank You
www.UCIexpress.org